## Slide 1: Assembly Language: Arithmetic and logic instructions
CSE 315
Microprocessors, Microcontrollers, and Embedded Systems

## Slide 2: AND, OR AND XOR
Syntax
AND destination, source
OR destination, source
XOR destination, source
The restrictions of destination and source are the same as ADD or SUB instructions

## Slide 3: AND, OR AND XOR
Effect on flags
SF, ZF, PF reflect the result
AF is undefined
CF, OF = 0

## Slide 4: AND, OR AND XOR
Example
XOR AX, AX
OR AL, 81h
AND AL, 7Fh
Clearing a Register
Set the MSB and LSB while preserving other bits
Clear the Sign Bit

## Slide 5: AND, OR AND XOR
Example

## Slide 6: NOT Instruction
Works on a single operand
Performs one’s complement operation on the destination
Syntax
NOT destination

## Slide 7: TEST Instruction
Performs similarly to the AND instruction
Except doesn’t write the output on the destination.
Only sets or resets the flags
Syntax
TEST destination, source
Usually used for flow control

## Slide 8: TEST Instruction
Example
TEST AL,1
Testing a number is even or not

## Slide 9: Shift / Rotate Instructions
Has two possible formats:
Opcode destination, 1
Opcode destination, CL
Effect on flags
SF, ZF, PF reflect the result
AF is undefined
CF value changes according to Shift / Rotate Type
OF =1 if result changes sign on last Shift / Rotation

## Slide 10: SHL and SAL instructions
Shifts the bits in the destination to the left
The MSB is shifted into CF
A 0 is shifted to LSB
SAL and SHL generate the same machine code
SHL and SAL

## Slide 11: SHL and SAL instructions
Example
If DH=8AH, CL=3
What is the result of
SHL DH, CL
If DX=8AH, CX=3
What is the result of
SHL DX, CX
DH=50H
CF=0
OF=0
DX=450H
CF=0
OF=0

## Slide 12: Multiplication Using SHL and SAL instructions
A Left shift on a binary number multiplies it by 2
Example
If DH=2H, CL=1
What is the result of
SHL DH, CL
DH=4H
CF=0
OF=0

## Slide 13: Overflow Flag Untrustworthy During Multiplication using SHL or SAL
Example
If DH=80H, CL=2
What is the result of
SHL DH, CL
DH=00H
CF=0
OF=0
CF and OF are not reliable for multiple shifts because multiple shifts are just a series of single shifts and CF, OF only reflect the result of the last shift.

## Slide 14: SHR and SAR instructions
Shifts the bits in the destination to the right
The LSB is shifted into CF
In case of SAR MSB retains its original value
SHR
SAR

## Slide 15: SHR and SAR instructions
SHR should be used for unsigned interpretation as it does not preserve sign
SAR should be used for signed interpretation as it preserves sign

## Slide 16: SHR and SAR instructions
Example
If AL=-15, CL=1
What is the result of
SHR AL, CL
If AL=-15, CL=1
What is the result of
SAR AL, CL
AL=120H
CF=1
OF=1
AL=-8
CF=1
OF=1

## Slide 17: Multiplication instructions
imul source
- Signed multiplication
  mul source
- Unsigned multiplication
Byte and Word Multiplication (A X B)
  If two bytes are multiplied, the result is a 16-bit word
    A: source
    B: al
    product: ax
  If two words are multiplied, the result is a 32-bit doubleword
    A: source
    B: ax
    Product (ms 16 bits): dx
    Product (ls 16 bits): ax

## Slide 18: Multiplication instructions
source can be a register or memory location (not a constant)
Byte form
  AX=AL*source
Word form
  DX:AX=AX*source
If ax contains 0001h and bx contains FFFFh
  mul bx; dx = 0000h ax = FFFFh
  imul bx ; dx = FFFFh ax = FFFFh (-1)

## Slide 19: Signed Multiplication
C
Assembly
Lable1:
short int x=0x8000;
short int y=0xFFFF;
x=x*y
Label1:
MOV x, 8000H
MOV y, FFFFH
MOV AX, x
MOV BX, y
IMUL BX

## Slide 20: Unsigned Multiplication
C
Assembly
Lable1:
unsinged short int x=0x8000;
unsigned short int y=0xFFFF;
x=x*y
Label1:
MOV x, 8000H
MOV y, FFFFH
MOV AX, x
MOV BX, y
MUL BX

## Slide 21: Multiplication instructions
Effect on flags
SF, ZF, AF, and PF Undefined
CF/OF
  MUL
    0: if upper half result 0
    1: Otherwise
  IMUL
    0: if upper half is sign extension of lower half.
    1: Otherwise

## Slide 22: More Examples
Instruction | Hex Product | DX | AX | CF/OF
MUL BX | FFFE0001 (4294836225) | FFFE (!zero) | 0001 | 1
IMUL BX | 1 | 0000 | 0001 | 0
AX=FFFFh,BX=FFFFh
AX=80h,BX=FFh
Instruction | Hex Product | AH | AL | CF/OF
MUL BX | 7F80 | 7F(!zero) | 80 | 1
IMUL BX | 0080 | 00 (no sign extension) | 80 | 1

## Slide 29: References
Ch 7, 9 Assembly Language Programming – by Yu and Marut